## Slide 1: Particle photon weather station Part 1 of 6: Overview & Event Hub Setup
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 2: Grab the slides & code:
http://aka.ms/ppws

## Slide 3: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 4
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 5
ppwsbssstorage
Storage Account
ppwsbssjob
Stream Analytics Job
ppwsbssns Service Bus Namespace
ppwsbsshub
Event Hub
SEND
PublishToEventHub Webhook
ppwsbssdata
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 6: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 7: Coming up with a good <name>
It’s recommended that you use a consistent prefix when you name your objects in Azure
Many names need to be globally unique. Plus, a good prefix makes it easier to identify them, determine their role, and delete them later when you need to clean up.
The prefix is identified by the “<name>” placeholders in the architecture diagram.
I recommend using something like “ppws” (short for ParticlePhotonWeatherStation) and your initials. For example, for me
“ppwsbss”

## Slide 8: Using the same region
As you provision your resources in Azure you should use the same region for all of them.
This will decrease latency between them as well as reduce costs by eliminating data leaving one region as it travels to another.

## Slide 9: Azure event hubs
“Azure Event Hubs is a highly scalable publish-subscribe service that can ingest millions of events per second and stream them into multiple applications.”
Learn more here:
https://azure.microsoft.com/services/event-hubs/

## Slide 10: Create the Azure Event Hub

## Slide 11: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 12: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 13: Particle photon weather station Part 2 of 6: Particle Cloud and photon Prep
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 14: Grab the slides & code:
http://aka.ms/ppws

## Slide 15: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 16: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 17: Particle “BUILD” browser IDE
https://build.particle.io

## Slide 18: The particle cloud
https://docs.particle.io/reference/api/

## Slide 19: The particle-CLI
https://docs.particle.io/reference/cli/
REQUIRES NODE.JS

## Slide 20: Claiming your Photon
https://docs.particle.io/guide/getting-started

## Slide 21: Configure the Particle Cloud and Photon

## Slide 22: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 23: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 24: Particle photon weather station Part 3 of 6: Photon DHT11 Circuit & WeBHOOK & CODE
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 25: Grab the slides & code:
http://aka.ms/ppws

## Slide 26: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 27: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 28: TWO TYPES OF DHT11 SENSORS
Standalone 4 Pin Sensor
(Requires external data line pullup resistor)
Pre-configured 3 Pin Sensor (Pullup resistor pre-installed on board)
Vcc
Data
Not Used
Gnd
Vcc
Data
Gnd

## Slide 29: Standalone sensor pullup resistor
Vcc
Data
Not Used
Gnd
10KΩ

## Slide 30: Standalone DHT11 CIRCUIT
10kΩ Pullup resistor Between the vcc pin and
the data pin

## Slide 31: Pre-configured sensor circuit

## Slide 32: Both use the same photon pins
PHOTON | DHT11
3V3 | Vcc
D2 | Data
GND | GND

## Slide 33: Creating the Photon and DHT11 Circuit

## Slide 34: Understanding the webhook
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
Webhook.json

## Slide 35
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}

## Slide 36
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
The name of the “event” that will invoke the webhook.
When you call Spark.publish(“PublishToEventHub", payload); from your Photon, the Particle cloud back end will trigger this webhook and publish your payload to the Azure Event Hub, specified by the “url”

## Slide 37
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
The “url” of the Azure Event Hub that the data will be published to.
You will need to enter your own Service Bus namespace and event hub names in place of the <YOUR_SERVICEBUS_NAME> and <YOUR_EVENTHUB_NAME> placeholders

## Slide 38
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
The data will be sent to the url using an HTTP POST

## Slide 39
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
The json template is used to create the data for the message that will be sent to the Azure Event Hub

## Slide 40
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
{
“s”: ”wthr”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “WearHacks LA”,
“d”: “Brets Demo Photon” “l”: “LA”,
} Sample Payload from the Photon’s Spark.Publish call

## Slide 41
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
The values:
SPARK_PUBLISHED_AT and SPARK_CORE_ID
Are supplied by the Particle cloud back end

## Slide 42
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
The Shared-Access-Signature key name, and key value used to access the Azure Event Hub

## Slide 43
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY"
},
"mydevices": true
}
Restricts the webhook to being triggered only from events published from your own devices

## Slide 44: Create the particle webhook
From the command prompt, get in the same folder as the webhook.json file you downloaded, and run: particle webhook create webhook.json
Other particle-cli webhook commands include: particle webhook list particle webhook delete hookid

## Slide 45: Creating the Webhook

## Slide 46: Groking the code

## Slide 47: Groking the code
// This #include statement was automatically added by the Spark IDE.
#include "Adafruit_DHT/Adafruit_DHT.h"
#define DHTPIN 2 // what pin we're connected to
// Uncomment whatever type you're using!
#define DHTTYPE DHT11// DHT 11
//...snip...
DHT dht(DHTPIN, DHTTYPE);

## Slide 48: Groking the code
char Org[] = "ORGANIZATION_NAME";
char Disp[] = "DISPLAY_NAME";
char Locn[] = "LOCATION";
//The amount of time (in milliseconds) to wait between each
//publication of data via the Particle WebHook
//Particle webhooks are rate limited to a maximum of 10/minute/device
//if we can only send 10 times a minute, that means we can send on average
//about once every six seconds, or 6000 milliseconds. So to avoid any
//rate limits by the particle cloud, keep the sendDelay at at least 6000.
int sendDelay = 6000;

## Slide 49: Groking the code
void setup()
{
dht.begin();
delay(10000);
}

## Slide 50: Groking the code
void loop()
{
// Reading temperature or humidity takes about 250 milliseconds!
// Sensor readings may also be up to 2 seconds 'old' (its a
// very slow sensor)
float h = dht.getHumidity();
// Read temperature as Celsius
float t = dht.getTempCelcius();
// Read temperature as Farenheit
float f = dht.getTempFarenheit();

## Slide 51: Groking the code
//Generate the temperature data payload
char payload[255];
snprintf(payload, sizeof(payload), "{ \"s\":\"wthr\", \"u\":\"F\", \"m\":\"Temperature\", \"v\": %f, \"o\":\"%s\", \"d\":\"%s\“,
\"l\":\"%s\"}",
f, Org, Disp, Locn);
//Send the temperature data payload
Spark.publish("PublishToEventHub", payload);
//Wait for the specified "sendDelay" before sending the humidity data...
delay(sendDelay);
{
“s”: ”wthr”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “ORGANIZATION_NAME”,
“d”: “DISPLAY_NAME” “l”: “LOCATION”,
}

## Slide 52: Groking the code
//Generate the humidity data payload
snprintf(payload, sizeof(payload), "{ \"s\":\"wthr\", \"u\":\"%%\", \"m\":\" Humidity \", \"v\": %f, \"o\":\"%s\", \"d\":\"%s\“,
\"l\":\"%s\"}",
h, Org, Disp, Locn);
//Send the humidity data payload
Spark.publish("PublishToEventHub", payload);
//wait for the specified "sendDelay" before looping...
delay(sendDelay);
}
{
“s”: ”wthr”,
“u”: “%”,
“m”: “Humidity”,
“v”: 60,
“o”: “ORGANIZATION_NAME”,
“d”: “DISPLAY_NAME” “l”: “LOCATION”,
}

## Slide 53: Monitoring your photon
Particle-cli: particle subscribe mine
Particle Dashboard: http://dashboard.particle.io/user/logs
Azure Portal: https://manage.windowsazure.com

## Slide 54: Deploying the code

## Slide 55: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 56: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 57: Particle photon weather station Part 4 0f 6: Reporting with Power BI
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 58: Grab the slides & code:
http://aka.ms/ppws

## Slide 59: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 60: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 61: Reporting with Power BI

## Slide 62: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 63: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 64: Particle photon weather station Part 5 of 6: RECEIVING EVENTS with Node.js
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 65: Grab the slides & code:
http://aka.ms/ppws

## Slide 66: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 67: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 68: Receiving Events Hub Messages with Node.js

## Slide 69: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 70: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
SEND
Receive

## Slide 71: Particle photon weather station Part 6 of 6: RECEIVING EVENTS with C#
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 72: Grab the slides & code:
http://aka.ms/ppws

## Slide 73: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 74: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
SEND
Receive

## Slide 75: Receiving Events Hub Messages with .NET

## Slide 76: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 77: Architecture overview
PublishWeather Web Hook
DeviceHub Event Hub
PowerBIDump Stream Analytics Job
WeatherData Power BI Data Set

## Slide 78: Architecture overview
PublishWeather Web Hook
DeviceHub Event Hub
PowerBIDump Stream Analytics Job
SensorData Power BI Data Set

## Slide 79: Power BI LOGO

## Slide 80: IoT Logo

## Slide 81: arduino

## Slide 82: GALILEO BOARD

## Slide 83: RASPBERRY PI

## Slide 84: FEZ SPIDER MAIN BOARD

## Slide 85: Sparkfun weather shield

## Slide 86: FEZ HAT

## Slide 87: Connect the dots azure icons
Microsoft Azure
Event Hubs
Stream Analytics
Storage blob
Storage table
SQL database
(
generic
)
Storage
(
Azure
)
Web App
Machine
Learning
GitHub code
Git repository
Service Bus
HDInsight

## Slide 88: LEDs

## Slide 89: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 90: cables

## Slide 91: More cables and adapters

## Slide 92: LEDs
Long Leg
Short Leg
Small Post
Big Post
Flat Edge
Vcc (+)
GND
Anode (+)
Cathode (-)

## Slide 93: LEDs

## Slide 94: Current limiting resistors
Providing more current than an LED is rated for can destroy the LED. To prevent that, you should use a “Current Limiting” resistor.
To calculate the value of the resistor you need to know the supply voltage (Usually 5V on the Arduino Uno), and the LEDs rated Forward Voltage (the voltage drop across the LED) and Forward Current (the maximum current the LED can handle).
The Arduino Uno has a built in current limiting resistor on Pin 13. If you use Pin 13 to power your LED you can use it without a separate resistor.

## Slide 95: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 96: Potentiometer – variable resistor

## Slide 97: breadboards
Breadboards offer a great way to prototype circuits. The provide a number of “buses” for connecting both power and components.
Power buses run the entire horizontal length
Component buses give you easy ways to connect pins together

## Slide 100: Micro SD Cards
Font: Segoe UI Semibold