## Slide 1: Particle photon weather station Part 1 of 6: Overview & Event Hub Setup
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 2: Grab the slides & code:
http://aka.ms/ppws

## Slide 3: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 4
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 5
ppwsbssstorage
Storage Account
ppwsbssjob
Stream Analytics Job
ppwsbssns Service Bus Namespace
ppwsbsshub
Event Hub
SEND
PublishToEventHub Webhook
ppwsbssdata
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 6: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 7: Coming up with a good <name>
It’s recommended that you use a consistent prefix when you name your objects in Azure
Many names need to be globally unique. Plus, a good prefix makes it easier to identify them, determine their role, and delete them later when you need to clean up.
The prefix is identified by the “<name>” placeholders in the architecture diagram.
I recommend using something like “ppws” (short for ParticlePhotonWeatherStation) and your initials. For example, for me
“ppwsbss”

## Slide 8: Using the same region
As you provision your resources in Azure you should use the same region for all of them.
This will decrease latency between them as well as reduce costs by eliminating data leaving one region as it travels to another.

## Slide 9: Azure event hubs
“Azure Event Hubs is a highly scalable publish-subscribe service that can ingest millions of events per second and stream them into multiple applications.”
Learn more here:
https://azure.microsoft.com/services/event-hubs/

## Slide 10: Create the Azure Event Hub

## Slide 11: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 12: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 13: Particle photon weather station Part 2 of 6: Particle Cloud and photon Prep
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 14: Grab the slides & code:
http://aka.ms/ppws

## Slide 15: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 16: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 17: Particle “BUILD” browser IDE
https://build.particle.io

## Slide 18: The particle cloud
https://docs.particle.io/reference/api/

## Slide 19: The particle-CLI
https://docs.particle.io/reference/cli/
REQUIRES NODE.JS

## Slide 20: Claiming your Photon
https://docs.particle.io/guide/getting-started

## Slide 21: Particle-cli login
You need to login to your particle cloud account from the cli (use your particle cloud login email and password): particle login
Of course you can also logout (provide your particle cloud password to completely logout): particle logout

## Slide 22: Identify the attached photon
First find the COM port it is attached to: particle serial list
Then, get the device ID: particle serial identify <COM#>
Copy the Photon ID to your clipboard and save somewhere for later
PHOTON CONNECTED VIA USB AND IN LISTENING MODE
(Blinking blue)

## Slide 23: Configure the particle wifi
From the command prompt: particle setup wifi Follow the prompts to connect the WiFi: <your wifi ssid> <your wifi security mode> <your wifi cypher type> <your wifi password>
PHOTON CONNECTED VIA USB AND IN LISTENING MODE
(Blinking blue)

## Slide 24: Claim and name your photon
Add the device to your account particle device add <id>
Name the device particle device rename <id> <newname>
PHOTON ONLINE (BREATHING CYAN)

## Slide 25: Configure the Particle Cloud and Photon

## Slide 26: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 27: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 28: Particle photon weather station Part 3 of 6: Photon DHT11 Circuit & WeBHOOK & CODE
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 29: Grab the slides & code:
http://aka.ms/ppws

## Slide 30: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 31: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 32: TWO TYPES OF DHT11 SENSORS
Standalone 4 Pin Sensor
(Requires external data line pullup resistor)
Pre-configured 3 Pin Sensor (Pullup resistor pre-installed on board)
Vcc
Data
Not Used
Gnd
Vcc
Data
Gnd

## Slide 33: Standalone sensor pullup resistor
Vcc
Data
Not Used
Gnd
10KΩ

## Slide 34: Standalone DHT11 CIRCUIT
10kΩ Pullup resistor Between the vcc pin and
the data pin

## Slide 35: Pre-configured sensor circuit

## Slide 36: Both use the same photon pins
PHOTON | DHT11
3V3 | Vcc
D2 | Data
GND | GND

## Slide 37: Creating the Photon and DHT11 Circuit

## Slide 38: Understanding the webhook
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
Webhook.json

## Slide 39
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}

## Slide 40
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The name of the “event” that will invoke the webhook.
When you call Particle.publish(“PublishToEventHub", payload); from your Photon, the Particle cloud back end will trigger this webhook and publish your payload to the Azure Event Hub, specified by the “url”

## Slide 41
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The “url” of the Azure Event Hub that the data will be published to.
You will need to enter your own Service Bus namespace and event hub names in place of the <YOUR_SERVICEBUS_NAME> and <YOUR_EVENTHUB_NAME> placeholders

## Slide 42
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The data will be sent to the url using an HTTP POST

## Slide 43
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The json template is used to create the data for the message that will be sent to the Azure Event Hub

## Slide 44
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
{
“s”: ”wthr”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “WearHacks LA”,
“d”: “Brets Demo Photon” “l”: “LA”,
} Sample Payload from the Photon’s Spark.Publish call

## Slide 45
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The values:
SPARK_PUBLISHED_AT and SPARK_CORE_ID
Are supplied by the Particle cloud back end

## Slide 46
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The Shared-Access-Signature key name, and key value used to access the Azure Event Hub

## Slide 47
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
Restricts the webhook to being triggered only from events published from your own devices

## Slide 48: Create the particle webhook
From the command prompt, get in the same folder as the webhook.json file you downloaded, and run: particle webhook create webhook.json
Other particle-cli webhook commands include: particle webhook list particle webhook delete hookid

## Slide 49: Creating the Webhook

## Slide 50: Groking the code

## Slide 51: Groking the code
// This #include statement was automatically added by the Spark IDE.
#include "Adafruit_DHT/Adafruit_DHT.h"
#define DHTPIN 2 // what pin we're connected to
// Uncomment whatever type you're using!
#define DHTTYPE DHT11// DHT 11
//...snip...
DHT dht(DHTPIN, DHTTYPE);

## Slide 52: Groking the code
char Org[] = "ORGANIZATION_NAME";
char Disp[] = "DISPLAY_NAME";
char Locn[] = "LOCATION";
//The amount of time (in milliseconds) to wait between each
//publication of data via the Particle WebHook
//Particle webhooks are rate limited to a maximum of 10/minute/device
//if we can only send 10 times a minute, that means we can send on average
//about once every six seconds, or 6000 milliseconds. So to avoid any
//rate limits by the particle cloud, keep the sendDelay at at least 6000.
int sendDelay = 6000;

## Slide 53: Groking the code
void setup()
{
dht.begin();
delay(10000);
}

## Slide 54: Groking the code
void loop()
{
// Reading temperature or humidity takes about 250 milliseconds!
// Sensor readings may also be up to 2 seconds 'old' (its a
// very slow sensor)
float h = dht.getHumidity();
// Read temperature as Celsius
float t = dht.getTempCelcius();
// Read temperature as Farenheit
float f = dht.getTempFarenheit();

## Slide 55: Groking the code
//Generate the temperature data payload
char payload[255];
snprintf(payload, sizeof(payload), "{ \"s\":\"wthr\", \"u\":\"F\", \"m\":\"Temperature\", \"v\": %f, \"o\":\"%s\", \"d\":\"%s\“,
\"l\":\"%s\"}",
f, Org, Disp, Locn);
//Send the temperature data payload
Particle.publish("PublishToEventHub", payload);
//Wait for the specified "sendDelay" before sending the humidity data...
delay(sendDelay);
{
“s”: ”wthr”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “ORGANIZATION_NAME”,
“d”: “DISPLAY_NAME” “l”: “LOCATION”,
}

## Slide 56: Groking the code
//Generate the humidity data payload
snprintf(payload, sizeof(payload), "{ \"s\":\"wthr\", \"u\":\"%%\", \"m\":\" Humidity \", \"v\": %f, \"o\":\"%s\", \"d\":\"%s\“,
\"l\":\"%s\"}",
h, Org, Disp, Locn);
//Send the humidity data payload
Particle.publish("PublishToEventHub", payload);
//wait for the specified "sendDelay" before looping...
delay(sendDelay);
}
{
“s”: ”wthr”,
“u”: “%”,
“m”: “Humidity”,
“v”: 60,
“o”: “ORGANIZATION_NAME”,
“d”: “DISPLAY_NAME” “l”: “LOCATION”,
}

## Slide 57: Monitoring your photon
Particle-cli: particle subscribe mine
Particle Dashboard: http://dashboard.particle.io/user/logs
Azure Portal: https://manage.windowsazure.com

## Slide 58: Deploying the code

## Slide 59: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 60: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 61: Particle photon weather station Part 4 0f 6: Reporting with Power BI
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 62: Grab the slides & code:
http://aka.ms/ppws

## Slide 63: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 64: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 65: Reporting with Power BI

## Slide 66: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 67: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 68: Particle photon weather station Part 5 of 6: RECEIVING EVENTS with Node.js
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 69: Grab the slides & code:
http://aka.ms/ppws

## Slide 70: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 71: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 72: Receiving Events Hub Messages with Node.js

## Slide 73: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 74: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
SEND
Receive

## Slide 75: Particle photon weather station Part 6 of 6: RECEIVING EVENTS with C#
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 76: Grab the slides & code:
http://aka.ms/ppws

## Slide 77: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 78: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
SEND
Receive

## Slide 79: Receiving Events Hub Messages with .NET

## Slide 80: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeReceiver”
Node.JS Receiver App
Receive
“DotNetReceiver”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 81: Architecture overview
PublishWeather Web Hook
DeviceHub Event Hub
PowerBIDump Stream Analytics Job
WeatherData Power BI Data Set

## Slide 82: Architecture overview
PublishWeather Web Hook
DeviceHub Event Hub
PowerBIDump Stream Analytics Job
SensorData Power BI Data Set

## Slide 83: Power BI LOGO

## Slide 84: IoT Logo

## Slide 85: arduino

## Slide 86: GALILEO BOARD

## Slide 87: RASPBERRY PI

## Slide 88: FEZ SPIDER MAIN BOARD

## Slide 89: Sparkfun weather shield

## Slide 90: FEZ HAT

## Slide 91: Connect the dots azure icons
Microsoft Azure
Event Hubs
Stream Analytics
Storage blob
Storage table
SQL database
(
generic
)
Storage
(
Azure
)
Web App
Machine
Learning
GitHub code
Git repository
Service Bus
HDInsight

## Slide 92: LEDs

## Slide 93: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 94: cables

## Slide 95: More cables and adapters

## Slide 96: LEDs
Long Leg
Short Leg
Small Post
Big Post
Flat Edge
Vcc (+)
GND
Anode (+)
Cathode (-)

## Slide 97: LEDs

## Slide 98: Current limiting resistors
Providing more current than an LED is rated for can destroy the LED. To prevent that, you should use a “Current Limiting” resistor.
To calculate the value of the resistor you need to know the supply voltage (Usually 5V on the Arduino Uno), and the LEDs rated Forward Voltage (the voltage drop across the LED) and Forward Current (the maximum current the LED can handle).
The Arduino Uno has a built in current limiting resistor on Pin 13. If you use Pin 13 to power your LED you can use it without a separate resistor.

## Slide 99: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 100: Potentiometer – variable resistor

## Slide 101: breadboards
Breadboards offer a great way to prototype circuits. The provide a number of “buses” for connecting both power and components.
Power buses run the entire horizontal length
Component buses give you easy ways to connect pins together

## Slide 104: Micro SD Cards
Font: Segoe UI Semibold