## Slide 1: Particle photon weather station Part 1 of 6: Overview & Event Hub Setup
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 2: Grab the slides & code:
http://aka.ms/ppws

## Slide 3: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 4: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 5: Coming up with a good <name>
It’s recommended that you use a consistent prefix when you name your objects in Azure
Many names need to be globally unique. Plus, a good prefix makes it easier to identify them, determine their role, and delete them later when you need to clean up.
The prefix is identified by the “<name>” placeholders in the architecture diagram.
I recommend using something like “ppws” (short for ParticlePhotonWeatherStation) and your initials. For example, for me
“ppwsbss”

## Slide 6: Using the same region
As you provision your resources in Azure you should use the same region for all of them.
This will decrease latency between them as well as reduce costs by eliminating data leaving one region as it travels to another.

## Slide 7: Azure event hubs
“Azure Event Hubs is a highly scalable publish-subscribe service that can ingest millions of events per second and stream them into multiple applications.”
Learn more here:
https://azure.microsoft.com/services/event-hubs/

## Slide 8: Create the Azure Event Hub

## Slide 9: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 10: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 11: Particle photon weather station Part 2 of 6: Particle Cloud and photon Prep
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 12: Grab the slides & code:
http://aka.ms/ppws

## Slide 13: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 14: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 15: Particle “BUILD” browser IDE
https://build.particle.io

## Slide 16: The particle cloud
https://docs.particle.io/reference/api/

## Slide 17: Claiming your Photon
https://docs.particle.io/guide/getting-started

## Slide 18: The particle-CLI
https://docs.particle.io/reference/cli/
REQUIRES NODE.JS

## Slide 19: Particle-cli login
You need to login to your particle cloud account from the cli (use your particle cloud login email and password): particle login
Of course you can also logout (provide your particle cloud password to completely logout): particle logout

## Slide 20: Identify the attached photon
First find the COM port it is attached to: particle serial list
Then, get the device ID: particle serial identify <COM#>
Copy the Photon ID to your clipboard and save somewhere for later
PHOTON CONNECTED VIA USB AND IN LISTENING MODE
(Blinking blue)

## Slide 21: Configure the particle wifi
From the command prompt: particle setup wifi Follow the prompts to connect the WiFi: <your wifi ssid> <your wifi security mode> <your wifi cypher type> <your wifi password>
PHOTON CONNECTED VIA USB AND IN LISTENING MODE
(Blinking blue)

## Slide 22: Claim and name your photon
Add the device to your account particle device add <id>
Name the device particle device rename <id> <newname>
PHOTON ONLINE (BREATHING CYAN)

## Slide 23: Configure the Particle Cloud and Photon

## Slide 24: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub

## Slide 25: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 26: Particle photon weather station Part 3 of 6: Photon DHT11 Circuit, WeBHOOK & CODE
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 27: Grab the slides & code:
http://aka.ms/ppws

## Slide 28: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 29: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 30: TWO TYPES OF DHT11 SENSORS
Standalone 4 Pin Sensor
(Requires external data line pullup resistor)
Pre-configured 3 Pin Sensor (Pullup resistor pre-installed on board)
Vcc
Data
Not Used
Gnd
Vcc
Data
Gnd

## Slide 31: Standalone sensor pullup resistor
Vcc
Data
Not Used
Gnd
10KΩ

## Slide 32: Standalone DHT11 CIRCUIT
10kΩ Pullup resistor Between the vcc pin and
the data pin

## Slide 33: Pre-configured sensor circuit

## Slide 34: Both use the same photon pins
PHOTON | DHT11
3V3 | Vcc
D2 | Data
GND | GND

## Slide 35: Creating the Photon and DHT11 Circuit

## Slide 36: GROKING the webhook
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
Webhook.json

## Slide 37: Groking the webhook
https://raw.githubusercontent.com/BretStateham/ParticlePhotonWeatherStation/master/Code/WebhookAndPhotonCode/webhook.json

## Slide 38
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}

## Slide 39
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The name of the “event” that will invoke the webhook.
When you call Particle.publish(“PublishToEventHub", payload); from your Photon, the Particle cloud back end will trigger this webhook and publish your payload to the Azure Event Hub, specified by the “url”

## Slide 40
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The “url” of the Azure Event Hub that the data will be published to.
You will need to enter your own Service Bus namespace and event hub names in place of the <YOUR_SERVICEBUS_NAME> and <YOUR_EVENTHUB_NAME> placeholders

## Slide 41
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The data will be sent to the url using an HTTP POST

## Slide 42
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The json template is used to create the data for the message that will be sent to the Azure Event Hub

## Slide 43
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
{
“s”: “Weather”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “Microsoft”,
“d”: “Bret’s PPWS” “l”: “San Diego”,
} Sample Payload from the Photon’s Particle.Publish call

## Slide 44
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The values:
SPARK_PUBLISHED_AT and SPARK_CORE_ID
Are supplied by the Particle cloud back end

## Slide 45
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
The Shared-Access-Signature key name, and key value used to access the Azure Event Hub

## Slide 46
{
"event": "PublishToEventHub",
"url": "https://<YOUR_SERVICEBUS_NAME>.servicebus.windows.net/<YOUR_EVENTHUB_NAME>/messages",
"requestType": "POST",
"json": {
"subject": "{{s}}",
"unitofmeasure": "{{u}}",
"measurename": "{{m}}",
"value": "{{v}}",
"organization": "{{o}}",
"displayname": "{{d}}",
"location": "{{l}}",
"timecreated": "{{SPARK_PUBLISHED_AT}}",
"guid": "{{SPARK_CORE_ID}}"
},
"azure_sas_token": {
"key_name": "<YOUR_SAS_POLICY_NAME>",
"key": "<YOUR_SAS_POLICY_KEY>"
},
"mydevices": true
}
Restricts the webhook to being triggered only from events published from your own devices

## Slide 47: Create the particle webhook
From the command prompt, get in the same folder as the webhook.json file you downloaded, and run: particle webhook create webhook.json
Other particle-cli webhook commands include: particle webhook list particle webhook delete hookid

## Slide 48: Creating the Webhook

## Slide 49: Groking the code
https://raw.githubusercontent.com/BretStateham/ParticlePhotonWeatherStation/master/Code/WebhookAndPhotonCode/particlephotonweatherstation.c

## Slide 50: Groking the photon code
// This #include statement was automatically added by the Spark IDE.
#include "Adafruit_DHT/Adafruit_DHT.h"
#define DHTPIN 2 // what pin we're connected to
// Uncomment whatever type you're using!
#define DHTTYPE DHT11// DHT 11
// ... Snip ...
DHT dht(DHTPIN, DHTTYPE);

## Slide 51: Groking the photon code
char Org[] = "ORGANIZATION_NAME";
char Disp[] = "DISPLAY_NAME";
char Locn[] = "LOCATION";
//The amount of time (in milliseconds) to wait between each
//publication of data via the Particle WebHook
//Particle webhooks are rate limited to a maximum of 10/minute/device
//if we can only send 10 times a minute, that means we can send on average
//about once every six seconds, or 6000 milliseconds. So to avoid any
//rate limits by the particle cloud, keep the sendDelay at at least 6000.
int sendDelay = 6000;

## Slide 52: Groking the photon code
void setup()
{
dht.begin();
Serial.begin(9600);
delay(10000);
}

## Slide 53: Groking the photon code
void loop()
{
// Reading temperature or humidity takes about 250 milliseconds!
// Sensor readings may also be up to 2 seconds 'old' (its a
// very slow sensor)
float h = dht.getHumidity();
// Read temperature as Celsius
float t = dht.getTempCelcius();
// Read temperature as Farenheit
float f = dht.getTempFarenheit();

## Slide 54: Groking the photon code
// Check if any reads failed. If any did, emit details to serial port for monitoring
// and exit the loop early (to try again).
if (isnan(h) || isnan(t) || isnan(f)) {
Serial.println("");
Serial.println("!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!");
Serial.println("Failed to read from DHT sensor!");
Serial.println("h=" + String(h) + " t=" + String(t) + " f=" + String(f));
Serial.println("!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!");
Serial.println("");
return;
} // Emit the sensor values to the Serial port for monitoring
Serial.println();
Serial.println("----------");
Serial.println();
Serial.println("h=" + String(h) + " t=" + String(t) + " f=" + String(f));

## Slide 55: Groking the photon code
// Generate the temperature data payload
char payload[255];
snprintf(payload, sizeof(payload), "{\"s\":\"Weather\", \"u\":\"F\", \"m\":\"Temperature\", \"v\": %f, \"o\":\"%s\", \"d\":\"%s\", \"l\":\"%s\"}", f,Org,Disp,Locn);
//Emit the payload to the serial port for monitoring purposes
Serial.println(payload);
// Send the temperature data payload
Particle.publish("PublishToEventHub", payload);
//Wait for the specified "sendDelay" before sending the humidity data...
delay(sendDelay);
{
“s”: “Weather”,
“u”: “F”,
“m”: “Temperature”,
“v”: 79.234,
“o”: “ORGANIZATION_NAME”,
“d”: “DISPLAY_NAME” “l”: “LOCATION”,
}

## Slide 56: Groking the photon code
// Generate the humidity data payload
snprintf(payload, sizeof(payload), "{\"s\":\"Weather\", \"u\":\"%%\", \"m\":\"Humidity\", \"v\": %f, \"o\":\"%s\", \"d\":\"%s\", \"l\":\"%s\"}", h,Org,Disp,Locn);
// Emit the payload to the serial port for monitoring purposes
Serial.println(payload);
// Send the humidity data payload
Particle.publish("PublishToEventHub", payload);
// wait for the specified "sendDelay" before looping...
delay(sendDelay); } // End of loop()
{
“s”: “Weather”,
“u”: “%”,
“m”: “Humidity”,
“v”: 25.345,
“o”: “ORGANIZATION_NAME”,
“d”: “DISPLAY_NAME” “l”: “LOCATION”,
}

## Slide 57: Monitoring photon via serial
particle serial monitor

## Slide 58: Monitoring webhook & event hub
Particle-cli: particle subscribe mine
Particle Dashboard: http://dashboard.particle.io/user/logs
Azure Portal: https://manage.windowsazure.com

## Slide 59: Deploying the code

## Slide 60: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook

## Slide 61: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 62: Particle photon weather station Part 4 0f 6: Reporting with Power BI
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 63: Grab the slides & code:
http://aka.ms/ppws

## Slide 64: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 65: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 66: WHAT IS POWER BI?
Online Service for creating and sharing data sets, visualizations, reports and dashboards both within your organization as well as with others.

## Slide 67: Signing up for power bi
You need an “organizational email” to sign up for Power BI.
You can’t use outlook.com, gmail.com, etc. personal accounts
Check out my blog post or Channel 9 video for more information
http://BretStateham.com/Using-power-bi-at-events

## Slide 68: Stream analytics
Stream Analytics is integrated out-of-the-box with Azure Event Hubs to ingest millions of events per second. Stream Analytics processes ingested events in real-time, comparing multiple streams or comparing streams with historical values and models. It detects anomalies, transforms incoming data, triggers an alert when a specific error or condition appears in the stream, and displays this real-time data in your dashboard.
https://azure.microsoft.com/services/stream-analytics/

## Slide 69: Stream analytics queries
https://msdn.microsoft.com/library/azure/dn834998.aspx
A Subset of T-SQL
Can take data in from either streams (Event Hubs) or static data (Blobs) or relational data (SQL Database)
Can join multiple streams. For example you could join event hub message data with relational data from a database
Can output data to a streams, static data, databases, or Power BI.
Has powerful windowing functions for creating aggregations over Tumbling, Hopping or Sliding time windows

## Slide 70: STREAM ANALYTICS INPUTS & OUTPUTS
<name>job
Stream Analytics Job
<name>hub
Event Hub
<name>data
Power BI Data Set
QUERY
SELECT
*
INTO
[OUTPUT]
FROM
[INPUT]
INPUT <name>hub
OUTPUT <name>data

## Slide 71: STREAM ANALYTICS INPUTS & OUTPUTS
ppwsbssjob
Stream Analytics Job
ppwsbsshub
Event Hub
ppwsbssdata
Power BI Data Set
QUERY
SELECT
*
INTO
ppwsbssdata
FROM
ppwsbsshub
INPUT
ppwsbsshub
OUTPUT
ppwsbssdata

## Slide 72: Groking the stream analytics query
https://raw.githubusercontent.com/BretStateham/ParticlePhotonWeatherStation/master/Code/StreamAnalyticsQuery/StreamAnalyticsQuery.txt

## Slide 73: Groking the stream analytics query
CREATE TABLE <name>hub (
coreid nvarchar(max),
data nvarchar(max),
displayname nvarchar(max),
event nvarchar(max),
EventEnqueuedUtcTime datetime,
EventProcessedUtcTime datetime,
guid nvarchar(max),
location nvarchar(max),
measurename nvarchar(max),
organization nvarchar(max),
PartitionId bigint,
published_at datetime,
subject nvarchar(max),
timecreated datetime,
unitofmeasure nvarchar(max),
value float
);
Issuing the “CREATE TABLE” statement before the query allows us to define the schema of the data. Any incoming messages that don’t meet this schema will be rejected. This helps prevent the Stream Analytics job from failing on invalid messages.
Notice that some of the fields are from the JSON payload generated by the Photon, and then the Particle Webhook (like measurename, unitofmeasure and value) while others are system generated values (like EventEnqueuedUtcTime or PartitionId)

## Slide 74: Groking the stream analytics query
SELECT
coreid
,displayname
,event
,EventEnqueuedUtcTime
,EventProcessedUtcTime
,guid
,location
,measurename
,organization
,PartitionId
,published_at
,subject
,timecreated
,unitofmeasure
,value
INTO
<name>data
FROM
<name>hub;
The “SELECT” statement defines the final values that will be output to the Power BI data set. We really aren’t taking much advantage of Stream Analytics processing capabilities here, we’re just forwarding the data long.
You could however be using Stream Analytics time windowing functions and SQL aggregations to generate summary values or even generate alert data based on data anomalies.
Event Hub source messages will come FROM
Power BI data set the data will be sent INTO

## Slide 75: Reporting with Power BI

## Slide 76: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
SEND
Receive

## Slide 77: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeClient”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 78: Particle photon weather station Part 5 of 6: RECEIVING EVENTS with Node.js
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 79: Grab the slides & code:
http://aka.ms/ppws

## Slide 80: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 81: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeClient”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 82: Azure-event-hubs repository
Azure Event Hub clients for
C
Java
Node.js
We’ll be using the “Node” client implementation in the upcoming demo.
https://github.com/Azure/Azure-event-hubs

## Slide 83: Azure-event-hubs NPM PACKAGE
Simplifies adding the Azure-Event-Hubs functionality to your Node packages
Depends on the Bluebird package’s promise implementation for async operations
npm install Bluebird
npm install Azure-Event-Hubs
https://www.npmjs.com/package/azure-event-hubs

## Slide 84: Visual studio code for node dev
Visual Studio Code is a great development environment for Node.js applications.
Not only can you edit your code in VS Code, but you can do step-through debugging as well as git source control integration. Check it out!
https://code.visualstudio.com/

## Slide 85: Groking the NODE CODE
https://raw.githubusercontent.com/BretStateham/ParticlePhotonWeatherStation/master/Code/NodeClient/app.js

## Slide 86: Groking the node code
'use strict';
var Promise = require('bluebird');
var EventHubClient = require('azure-event-hubs').Client;
var moment = require('moment');

## Slide 87: Groking the node code
// The Event Hubs SDK can also be used with an Azure IoT Hub connection string.
// In that case, the eventHubPath variable is not used and can be left undefined.
var connectionString = '[Event Hub Connection String]';
var eventHubPath = '[Event Hub Name (Path)]';
var client = EventHubClient.fromConnectionString(connectionString, eventHubPath);
// Set the consumer group and start time offset for the event hub receivers
// If you have created a consumer group for your node app to use, enter it here
var consumerGroup = '$Default';
// Set the consumer up to receive only new messages, not all the old ones as well
// set receiveAfterTime to null to read all of the messages from the beginning
var receiveAfterTime = Date.now() - 5000;

## Slide 88: Groking the node code
// Log a received message body out to the console
var printEvent = function (ehEvent) {
var body = ehEvent.body
var created = moment(body.timecreated);
var val = Number(body.value);
console.log(created.format("hh:mm:ss a") + " - " + body.measurename + ": " + val.toFixed(2) + body.unitofmeasure);
};
// Log an error to the console
var printError = function (err) {
console.error(err.message);
};

## Slide 89: Groking the node code
// Send the given eventBody to the Event Hub
var sendEvent = function (eventBody) {
return function (sender) {
console.log('Sending Event: ' + eventBody);
return sender.send(eventBody);
};
};

## Slide 90: Groking the node code
client.open()
.then(client.getPartitionIds.bind(client))
.then(function (partitionIds) {
return partitionIds.map(function (partitionId) {
return client.createReceiver(
consumerGroup,
partitionId,
{ 'startAfterTime': receiveAfterTime }
).then(function (receiver) {
receiver.on('errorReceived', printError);
receiver.on('message', printEvent);
});
});
})

## Slide 91: Groking the node code
// The send commands have been commented out since we want to just receive
// messages from the Photon sender, but you can see how you could use this code
// to send messages as well..
// .then(client.createSender.bind(client))
// .then(sendEvent('foo'))
.catch(printError);

## Slide 92: Receiving Events Hub Messages with Node.js

## Slide 93: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeClient”
Node.JS Receiver App
Receive
SEND
Receive

## Slide 94: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
SEND
Receive

## Slide 95: Particle photon weather station Part 6 of 6: RECEIVING EVENTS with C#
Particle Photon + DHT11 Sensor + Azure + Power BI + Node.js + .NET = AWESOME

## Slide 96: Grab the slides & code:
http://aka.ms/ppws

## Slide 97: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 98: Solution ARCHITECTURE
<name>ns Service Bus Namespace
<name>hub
Event Hub
PublishToEventHub Webhook
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>data
Power BI Data Set
Logging
Send
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
SEND
Receive

## Slide 99: .NET Event hub client tutorial
Get started using Event Hubs from C#. This tutorial helps you create both a sender and a receiver using the “Microsoft Azure Service Bus” and “Microsoft Azure Service Bus Event Hub - EventProcessorHost” NuGet packages.
http://aka.ms/ehcs

## Slide 100: Azure storage requirement
The Node.js sample app didn’t require an Azure Storage Account.
The Azure-Event-Hubs node client doesn’t have any built-in “checkpointing” that allows clients to pick up where they left off.
If you want that behavior, you have to implement it yourself. You could CHOOSE to use Azure Storage as a place to store that checkpoint data, but that is up to you

## Slide 101: Azure storage requirement
The EventProcessHost class provided by Microsoft for .NET clients though DOES have built-in checkpointing, and it REQUIRES an Azure Storage account to store that checkpoint data in.
If you prefer to not use Azure Storage you will need to implement your own .NET client using the Azure Service Bus or AMQP apis.

## Slide 102: Groking the .NET CODE
https://github.com/BretStateham/ParticlePhotonWeatherStation/tree/master/Code/NetClient

## Slide 103: Groking the .net code
Message.cs defines the data structure. Each message from our Photon (via the Particle Cloud and the Event Hub) will end up in one of these.
SimpleEventProcessor.cs handles the opening and closing of an Event Hub partition, and the de-serializing of received messages into Message instances
Program.cs is the main console app program. It initializes the EventProcessorHost with the Event Hub and Storage Account settings and kicks off the receiving of messages.

## Slide 104: Groking the .nET code - Message.cs
public class Message
{
// ...snip...
private string unitOfMeasure;
public string UnitOfMeasure
{
get { return unitOfMeasure; }
set { unitOfMeasure = value; }
}
private string measureName;
public string MeasureName
{
get { return measureName; }
set { measureName = value; }
}
private float value;
public float Value
{
get { return value; }
set { this.value = value; }
}
// ...snip...
}
The “Message” class is used to de-serialize the JSON data received from the event hub.
The various properties we published from the Photon via the Particle Cloud, like “measurename”, “unitofmeasure”, “value”, etc. get de-serialized into this strongly typed object for easy use.
Cool, eh!?

## Slide 105: Groking the .nET code - SimpleEventProcessor.cs
class SimpleEventProcessor : IEventProcessor
{
Stopwatch checkpointStopwatch;
public Task OpenAsync(PartitionContext context)
{
Console.WriteLine(
"SimpleEventProcessor initialized. Partition: '{0}', Offset: '{1}'", context.Lease.PartitionId, context.Lease.Offset);
checkpointStopwatch = new Stopwatch();
checkpointStopwatch.Start();
return Task.FromResult<object>(null);
}

## Slide 106: Groking the .nET code - SimpleEventProcessor.cs
public async Task CloseAsync(PartitionContext context, CloseReason reason)
{
Console.WriteLine(
"Processor Shutting Down. Partition: '{0}', Reason: '{1}'", context.Lease.PartitionId, reason);
if (reason == CloseReason.Shutdown)
{
await context.CheckpointAsync();
}
}

## Slide 107: Groking the .nET code - SimpleEventProcessor.cs
public async Task ProcessEventsAsync(PartitionContext context, IEnumerable<EventData> messages)
{
foreach (EventData eventData in messages)
{

## Slide 108: Groking the .nET code - SimpleEventProcessor.cs
try
{
Message message;
string data = Encoding.UTF8.GetString(eventData.GetBytes());
message = JsonConvert.DeserializeObject<Message>(data);
Console.WriteLine(string.Format("{0:hh:mm:ss tt} - {1}: {2:0.00}{3}", message.TimeCreated.ToLocalTime(), message.MeasureName, message.Value, message.UnitOfMeasure));
}
catch (Exception ex)
{
string exMessage = string.Format( "\n!!!!!!!!!!\nA {0} occurred when deserializing the message: \n{1}\n!!!!!!!!!!\n", ex.GetType().Name, ex.Message);
Console.WriteLine(exMessage);
Debug.WriteLine(exMessage);
}

## Slide 109: Groking the .nET code - SimpleEventProcessor.cs
// Call checkpoint every five minutes, so that worker can resume processing // from 5 minutes back if it restarts.
if (this.checkpointStopwatch.Elapsed > TimeSpan.FromMinutes(5))
{
await context.CheckpointAsync();
this.checkpointStopwatch.Restart();
}
} // End foreach loop
} // End ProcessEventsAsync method } // SimpleEventProcessor class

## Slide 110: Groking the .nET code - PROGRAM.cs
class Program
{
static void Main(string[] args)
{
string eventHubConnectionString = "[Event Hub Connection String]";
string eventHubName = "[Event Hub Name (Path)]";
string consumerGroupName = EventHubConsumerGroup.DefaultGroupName;
string storageAccountName = "[Storage Account Name]";
string storageAccountKey = "[Storage Account Key]";
string storageConnectionString = string.Format( "DefaultEndpointsProtocol=https;AccountName={0};AccountKey={1}", storageAccountName, storageAccountKey);
string eventProcessorHostName = Guid.NewGuid().ToString();
EventProcessorHost eventProcessorHost = new EventProcessorHost(
eventProcessorHostName, eventHubName, consumerGroupName, eventHubConnectionString, storageConnectionString);

## Slide 111: Groking the .nET code - PROGRAM.cs
Console.WriteLine("Registering EventProcessor...");
EventProcessorOptions processorOptions = new EventProcessorOptions()
{
// Start reading messages from now, ingore any previous messages in the hub
// Set initialOffsetProvider = null if you don’t want to use an offset.
// Normal EventProcessorHost checkpointing should then read from where we last processed
InitialOffsetProvider = (name) => DateTime.UtcNow
};
eventProcessorHost.RegisterEventProcessorAsync<SimpleEventProcessor>(processorOptions).Wait();
Console.WriteLine("Receiving. Press enter key to stop worker.");
Console.ReadLine();
eventProcessorHost.UnregisterEventProcessorAsync().Wait();
} // End of Main()
} // End of Program class

## Slide 112: Receiving Events Hub Messages with .NET

## Slide 113: Solution ARCHITECTURE
<name>storage
Storage Account
<name>job
Stream Analytics Job
<name>ns Service Bus Namespace
<name>hub
Event Hub
SEND
PublishToEventHub Webhook
<name>data
Power BI Data Set
“NodeClient”
Node.JS Receiver App
Receive
“NetClient”
.NET C# Console App Receiver
Receive
ChkPt
Logging
Receive
Send

## Slide 114: Architecture overview
PublishWeather Web Hook
DeviceHub Event Hub
PowerBIDump Stream Analytics Job
WeatherData Power BI Data Set

## Slide 115: Architecture overview
PublishWeather Web Hook
DeviceHub Event Hub
PowerBIDump Stream Analytics Job
SensorData Power BI Data Set

## Slide 116: Power BI LOGO

## Slide 117: IoT Logo

## Slide 118: arduino

## Slide 119: GALILEO BOARD

## Slide 120: RASPBERRY PI

## Slide 121: FEZ SPIDER MAIN BOARD

## Slide 122: Sparkfun weather shield

## Slide 123: FEZ HAT

## Slide 124: Connect the dots azure icons
Microsoft Azure
Event Hubs
Stream Analytics
Storage blob
Storage table
SQL database
(
generic
)
Storage
(
Azure
)
Web App
Machine
Learning
GitHub code
Git repository
Service Bus
HDInsight

## Slide 125: LEDs

## Slide 126: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 127: cables

## Slide 128: More cables and adapters

## Slide 129: LEDs
Long Leg
Short Leg
Small Post
Big Post
Flat Edge
Vcc (+)
GND
Anode (+)
Cathode (-)

## Slide 130: LEDs

## Slide 131: Current limiting resistors
Providing more current than an LED is rated for can destroy the LED. To prevent that, you should use a “Current Limiting” resistor.
To calculate the value of the resistor you need to know the supply voltage (Usually 5V on the Arduino Uno), and the LEDs rated Forward Voltage (the voltage drop across the LED) and Forward Current (the maximum current the LED can handle).
The Arduino Uno has a built in current limiting resistor on Pin 13. If you use Pin 13 to power your LED you can use it without a separate resistor.

## Slide 132: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 133: Potentiometer – variable resistor

## Slide 134: breadboards
Breadboards offer a great way to prototype circuits. The provide a number of “buses” for connecting both power and components.
Power buses run the entire horizontal length
Component buses give you easy ways to connect pins together

## Slide 137: Micro SD Cards
Font: Segoe UI Semibold